## Slide 1
EDL PROJECT - PART II
DVB-S2X DIGITAL BASEBAND RECEIVER
TEAM MEMBERS
Bhavesh Mali Varshith K Member Name 3
FACULTY MENTOR
Prof. Rajshekhar V Bhat

## Slide 2
PROJECT OBJECTIVE
PROBLEM STATEMENT
Design and implement a complete DVB-S2X digital baseband receiver backend (Part II) targeting the RFSoC platform. The system must process complex I/Q samples from an existing transmitter and recover the original video stream.
PRIMARY GOAL
Achieve real-time LDPC/BCH decoding and valid Transport Stream (TS) generation to display live video on a hardware monitor.

## Slide 3
Transmitter end Architecture

## Slide 4
Receiver-end architecture

## Slide 5
Our block on at RX end

## Slide 6
SPECIFICATIONS
MINIMUM REQUIREMENTS
DESIRABLE SPECIFICATIONS
Platform: Xilinx Zynq UltraScale+ RFSoC.
Input: Complex I/Q Baseband Samples.
Core Blocks: LDPC Decoder, BCH Decoder, Descrambler.
Output: Valid MPEG-TS Transport Stream.
Performance: Real-time processing for standard definition video.
Integration: Seamless interface with Part I frontend.
High Throughput: Support for High Bitrate.
Advanced Features: Adaptive Coding and Modulation (ACM) support.
Optimization: Low resource utilization (LUT/BRAM) on FPGA.
Latency: Minimal processing latency for live streaming.
Debug: Integrated ILA (Integrated Logic Analyzer) for real-time constellation viewing.

## Slide 7
PROJECT ROADMAP
Design & Sim: LDPC, BCH, Demapper
FPGA Synthesis, Timing Closure, Unit Tests
Merge with Part I, On-board Debugging
Final Video Demonstration
Weeks 1-3
Weeks 4-6
Weeks 7-9
Week 10

## Slide 8
TASK PLAN: WEEKS 1-3
MEMBER 1
Focus: Forward Error Correction (FEC) - Part A
Responsible for the core LDPC Decoder, the most computationally intensive block of the receiver.
Week 1: Literature review of DVB-S2X LDPC parity check matrices and standard specifications. Select decoding algorithm (Sum-Product vs. Min-Sum).
Week 2: Develop fixed-point model in Python/MATLAB to determine bit-width requirements.
Week 3: Begin Verilog/Chisel implementation of the Check Node (CN) and Variable Node (VN) processing units.

## Slide 9
TASK PLAN: WEEKS 1-3
MEMBER 2
Focus: FEC - Part B & Interleaving
Responsible for handling the stream before and after LDPC, including demapping and outer decoding.
Week 1: Implement Soft-Output Constellation Demapper (QPSK, 8PSK, etc.) to generate Log-Likelihood Ratios (LLRs).
Week 2: Design the Bit Deinterleaver memory structure to match standard block interleaving patterns.
Week 3: Implement BCH Decoder (Bose–Chaudhuri–Hocquenghem) for cleaning up residual error floors after LDPC.

## Slide 10
TASK PLAN: WEEKS 1-3
MEMBER 3
Focus: System Integration & Framing
Responsible for extracting the data stream and preparing the interface for Part I.
Week 1: Define AXI-Stream interfaces between blocks. Create common testbench framework.
Week 2: Implement BBFRAME extraction logic (interpreting the BBHEADER).
Week 3: Implement CRC-8 verification module and the final Transport Stream (TS) generation logic (Un-packetizing to MPEG-TS).

## Slide 11
COORDINATION STRATEGY
Part I Interface
Weekly sync with Part I team to align on I/Q data format and control signals (Valid/Ready handshakes).
Version Control
Unified Git repository with branch protection rules. Code reviews required before merging to main.
Hardware Testing
Early access to RFSoC board in lab to verify simple loopback tests before full deployment.

## Slide 12
QUESTIONS?
Thank you for your attention. We are ready to begin the implementation phase.

## Slide 13
IMAGE SOURCES
https://i.pcmag.com/imagery/articles/00TEICwymxxCA88jgemSyVY-1..v1651090630.jpg
Source: www.pcmag.com
https://blog.adigo.com/wp-content/uploads/2021/08/collaboration-meeting.jpg
Source: blog.adigo.com
https://www.amd.com/content/dam/amd/en/images/products/boards/2410750-zynq-ultrascale-rfsoc-xczu48dr-board-product.jpg
Source: www.amd.com
https://it.mathworks.com/help/examples/satcom/win64/DVBS2XRegularModeBitErrorRateExample_03.png
Source: it.mathworks.com
https://cdnb.ganttpro.com/uploads/2021/10/roadmapping-in-roadmunk-1024x625.png
Source: blog.ganttpro.com